## Slide 1
Detection of Internal Fractures in Sandstone Specimens with CNN and U-Net
Changdi He
Department of Mining Engineering
Page 1

## Slide 2
Introduction & Objective
01
Results & Discussion
03
Methodology & Procedure
02
Conclusions & Future work
04
THE MAIN CONTENTS

## Slide 3
1
Part
Introduction & Objective

## Slide 4
Part 1
Introduction
Image of a rock test
(Shimizu et al., 2000)
（b) Comparison of different fracture analysis methods
(Yang et al. 2021)
（c) Image of X-ray CT equipment (Zhou et al. 2021)
How to detect the cracks in hundreds of 2D CT images?
Cracks
Image credit: https://www.soogif.com/materialPage/0zzGcnLOvvg
Page 4

## Slide 5
Part 1
Objective
Sandstone sample
(Yang et al. 2021)
Note: The ResUNet Python code was cited from:
https://github.com/Subham2901/Concrete_Crack_Segmentation/blob/master/Notebooks/Deep_crack.ipynb
Cracks
(b) Selected 2D CT images of sandstone sample
(6 out of 937) (Yang et al. 2021)
How to detect the cracks in hundreds of 2D CT images?
Try U-Net!!!
Standard U-Net
Residual U-Net (ResUNet)
Residual U-Net-Transfer Learning
(ResUNet-TL)
Image credit: https://cn.phoneky.com/gif-animations/?id=s2s101943
Page 5

## Slide 6
2
Part
Methodology & Procedure

## Slide 7
Part 2
Methodology: Standard U-Net – architecture and loss function
Input
1
16
16
Output
2562
1282
642
322
162
32
32
64
64
128
128
256
256
162
256
256
256
128
128
64
64
32
32
16
128
256
128
64
322
642
1282
2562
64
32
16
Conv 3×3, ReLu
MaxPooling 2×2
Up-conv 3×3
Conv 1×1, Sigmoid
Concatenate
Loss function: Binary cross-entropy
where:
L(y, p) represents the binary cross-entropy loss
y is the true label (either 0 or 1)
p is the predicted probability for class 1
(i.e., the output of the sigmoid activation function)
Page 7
d=0.1
d=0.1
d=0.2
d=0.5
d=0.2
d=0.2
d=0.2
d=0.1
d=0.1
Dropout rate: d

## Slide 8
Part 2
Methodology: ResUNet – architecture and loss function
Loss function: Dice loss
D
where:
y is the ground truth binary mask;
p is the predicted binary mask;
|y| and |p| represent the sum of all elements in y and p, respectively;
|y ∩ p| represents the sum of the element-wise product of y and p.
Input
16
Output
2562
1282
642
322
162
32
64
128
256
256
162
128
16
128
322
642
1282
2562
64
Conv 3×3, ReLu
MaxPooling 2×2
Up-conv 3×3
Conv 1×1, Sigmoid
Concatenate
E1
E2
E3
E4
E5
256
b0
b1
128
128
64
32
64
32
32
16
2562
Residual block
Dice coefficient
Page 8
Dropout rate: 0.5

## Slide 9
Part 2
Methodology: Residual U-Net with transfer learning techniques (ResUNet-TL)– architecture and loss function
Input
64
Output
2562
1282
642
322
162
128
256
512
512
512
162
512
64
512
322
642
1282
2562
256
Conv 3×3, ReLu
MaxPooling 2×2
Up-conv 3×3
Conv 1×1, Sigmoid
Concatenate
E1
E2
E3
E4
E5
512
b0
b1
512
512
256
128
256
128
128
64
2562
Residual block
VGG16 block
Loss function: Dice loss
D
where:
y is the ground truth binary mask;
p is the predicted binary mask;
|y| and |p| represent the sum of all elements in y and p, respectively;
|y ∩ p| represents the sum of the element-wise product of y and p.
Dice coefficient
Page 9
Dropout rate: 0.5

## Slide 10
Part 2
Procedure
Label some CT images
Resize, normalize, and augment data
Design U-Net-based models
Split the dataset (Training, validating and testing)
Train, evaluate, and test the UNet
Without cracks
With cracks
Labeled image
Binary image
Labeled image
Binary image
340 images without cracks
597 images with cracks
= 0.57
Training (70%), Validation (15%), and testing data (15%).
Develop U-Net based models: Standard U-Net, ResNet, ResNet-TL
  Add L2 regulation
  Add dropout technique
143 images without cracks
265 images with cracks
= 0.54
Page 10

## Slide 11
Part 2
Procedure
Label some CT images
Resize, normalize, and augment data
Design U-Net-based models
Split the dataset (Training, validating and testing)
Train, evaluate, and test the models
Resize, normalize, and augment data:
  Resize the input images as 256×256;
  Batch size: 32
  Normalize the input image pixel value to the range of [0,1]
Page 11

## Slide 12
3
Part
Results & Discussion

## Slide 13
Part 3
Predicted results – U-Net, ResUNet, ResUNet-TL
U-Net
ResUNet
ResUNet-TL
Page 13

## Slide 14
Part 3
Comparison of different accuracy and loss curves
U-Net
ResUNet
ResUNet-TL
Accuracy
Accuracy
Accuracy
Loss
Loss
Loss
Page 14

## Slide 15
Part 3
U-Net
ResUNet
ResUNet-TL
IOU
IOU
IOU
Dice coefficient
Dice coefficient
Dice coefficient
IOU: Intersection over Union
IOU = (Intersection area) / (Union area)
Dice coefficient: Measures the similarity between two sets.
(2 ∗ |𝑦 ∩ 𝑝|))/((|𝑦|+ |𝑝|)
Page 15
Comparison of different IOU and Dice coefficient curves

## Slide 16
Confusion Matrix
U-Net |  | True |  | ResUNet |  | True |  | ResUNet-TL |  | True | 
 |  | + | - |  |  | + | - |  |  | + | -
Predicted | + | 399332 | 8546 | Predicted | + | 4022838 | 6683 | Predicted | + | 4014719 | 3545
 | - | 12663 | 48701 |  | - | 9796 | 23915 |  | - | 12272 | 32696
Part 3
Accuracy: (TP + TN) / (TP + TN + FP + FN)
Precision: TP / (TP + FP)
Recall (Sensitivity): TP / (TP + FN)
Specificity: TN / (TN + FP)
F1 Score:
2 * (Precision * Recall) / (Precision + Recall)
[[True Negatives (TN) False Positives (FP)]
[False Negatives (FN) True Positives (TP)]]
 | U-Net | ResUNet | ResUNet-TL
Accuray | 0.955 | 0.996 | 0.996
Precision | 0.851 | 0.782 | 0.902
Sensitivity | 0.794 | 0.709 | 0.727
Specificity | 0.979 | 0.998 | 0.999
F1 Score | 0.821 | 0.744 | 0.805
✔
Page 16

## Slide 17
Application of the ResUNet-TL model
Part 3
Labeling rest of the CT images using the ResUNet-TL model
Page 17

## Slide 18
Discussion
Part 3
(a) Epoch = 100
(b) Epoch = 200
1. Selecting an appropriate number of epochs is crucial.
2. Imbalanced data can lead to biased learning, and L2 regulation can prevent overfitting.
3. The number of the feature map can influence the model performance.
(a) Standard UNet
(b) ResUNet
(c) ResUNet-TL
(a) Imbalanced data and without L2 regulation
(b) Balanced data and with L2 regulation
Page 18

## Slide 19
4
Part
Conclusions & Future work

## Slide 20
Conclusions & Future work
Part 4
Conclusions:
  UNet-based models have demonstrated their applicability in detecting a large number of CT images.
  ResUNet-TL is relatively more suitable for this particular project.
  Appropriate number of epochs is important for optimal model performance.
  Imbalanced data can result in biased learning.
  L2 regularization yields a simpler model that is less prone to overfitting the training data.
  Increasing the number of feature maps allows the model to learn more complex features, but it also results in higher computational costs.
Future work:
  Expand the dataset for further training and refinement of the developed models.
  Conduct segmenting multiple classes within CT images.
  Implementation of 3D reconstruction techniques.
Page 20

## Slide 21
References
Detection of Internal Fractures in Sandstone Specimens with CNN and U-Net
Yang, B., Wang, H., Wang, B., Shen, Z., Zheng, Y., Jia, Z., & Yan, W. (2021). Digital quantification of fracture in full-scale rock using micro-CT images: A fracturing experiment with N2 and CO2. Journal of Petroleum Science and Engineering, 196, 107682.
Shimizu, T., & Tachibana, E. A Study On Uniaxial Compressive Strength Of Plain Concrete Under Dynamic Cyclic Loading.
Zhou, X. P., Jiang, D. C., & Zhao, Z. (2021). Digital Evaluation of Micro-Pore Water Effects on Mechanical and Damage Characteristics of Sandstone Subjected to Uniaxial, Cyclic Loading–Unloading Compression by 3D Reconstruction Technique. Rock Mechanics and Rock Engineering, 1-21.
Liu, Y., Yao, J., Lu, X., Xie, R., & Li, L. (2019). Deep Crack: A deep hierarchical feature learning architecture for crack segmentation. Neurocomputing, 338, 139-153.
Page 21

## Slide 22
Question?
Thank you!